## Slide 1: 3DGATES: An Instruction-Level Energy Analysis and Optimization of 3D-Printers
Jerry Ajay, Chen Song, Aditya Singh Rathore, Chi Zhou, Wenyao Xu

## Slide 2: Instruction-Level Energy Analysis
Why energy analysis for 3D Printers?
Why an instruction-level approach?

## Slide 3
Why energy analysis for 3D Printers?
Emergence of Energy Constrained 3D Printers

## Slide 4
3D Printing Using Smartphone
http://www.ono3d.net/
Energy Constrained 3D Printing
Energy Constrained
Made in Space Project
http://www.madeinspace.us/
3D Printing Medical Components in Remote Locations
https://www.inverse.com/article/20840-how-3d-printers-are-saving-lives-in-remote-parts-of-the-world

## Slide 5: 3DGATES: An Instruction-Level Energy Analysis and Optimization of 3D-Printers
Why an instruction-level approach?
Easy Energy optimizations
Why energy analysis for 3D Printers?
Emergence of Energy Constrained 3D Printers

## Slide 6
Why instruction-level energy optimizations?
Independent of different H/W specifications
Assigns accurate power costs
to S/W
Instruction Level Energy Optimizations
Compiler Level
Hardware Level
Instr-Level

## Slide 7
Why an instruction-level approach?
Why energy analysis for 3D Printers?
Emergence of Energy Constrained 3D Printers
In this work,
1. We quantify 3D printing energy consumption.
AND
2. Identify Power Hungry components.
AND
3. Reduce energy consumption by 25%.
Original Energy
New Energy
Common Interface for Energy optimizations

## Slide 8
Talk Outline
Application
Layer
Compiler
Layer
Firmware
Layer
STL
G-code
Signal
Hardware
Layer
1. Background
2. Instruction-level Energy Analysis
Instruction
Support
Firmware
Support
Compiler
Support
3. Cross-layered Energy Optimizations
4. Evaluation
Square Circles
Lines
Grid
Triangles

## Slide 9
Talk Outline
Application
Layer
Compiler
Layer
Firmware
Layer
STL
G-code
Signal
Hardware
Layer
1. Background
2. Instruction-level Energy Analysis
Instruction
Support
Firmware
Support
Compiler
Support
3. Cross-layered Energy Optimizations
4. Evaluation
Square Circles
Lines
Grid
Triangles

## Slide 10
Background – 3D Printing Process
Application
Layer
STL
Compiler
Layer
G-code
Firmware
Layer
Signal
Hardware
Layer
CYBER LAYER
PHYSICAL LAYER

## Slide 11
Talk Outline
Application
Layer
Compiler
Layer
Firmware
Layer
STL
G-code
Signal
Hardware
Layer
1. Background
2. Instruction-level Energy Analysis
Instruction
Support
Firmware
Support
Compiler
Support
3. Cross-layered Energy Optimizations
4. Evaluation
Square Circles
Lines
Grid
Triangles

## Slide 12
G-code Instructions - Overview
Types of G-codes:
G0-Type (Align Instructions):
  Speed: 7200 mm/min
G1-Type (Material Extrusion Instructions):
  Speed: 1200 – 8600 mm/min
C-Type (Control Instructions):
  - Heater, Fan controls
Instruction Level Energy Analysis (1/5)
Instruction Distribution in a typical G-code file
Instruction Category | Count | %
G0-Type | 36184 | 13.86%
G1-Type | 224837 | 86.13%
C-Type | 5 | 0.001%
Total | 261026 | 100%

## Slide 13
Instruction Category | Avg. Pwr. (W)
G0 7200 mm/min | 21.30
G1 1200 mm/min | 37.90
G1 3600 mm/min | 39.94
G1 5200 mm/min | 40.38
G1 8600 mm/min | 42.06
M109: Heater Temp | 31.19
M106: Fan on | 3.61
Instruction Level Energy Analysis (2/5)
Experimental Setup to measure G-code Power Consumption
G0-Type
G1-Type
C-Type
Infinite Looping Individual Instructions to Obtain Avg. Power

## Slide 14
Instruction Level Energy Analysis (3/5)
Measure current using WattsUp
Calculate distance moved
Calculate energy consumed by instr.
Summation of all instr. energies.
Energy Model

## Slide 15
Chart: 
Instruction-Level Energy Analysis (4/5)
HEAT UP
PRINTING
POWER (W)
Insight: An Instruction level energy simulator is accurate for energy simulations for 3D Printing.
Based on Instruction Level Energy Model we built a S/W Energy Simulator
COOL DOWN
IDLE
Error approx. 3%

## Slide 16
Instruction-Level Energy Analysis (5/5)
Benchmark Statistics
Simulation over 338 Designs downloaded from
www.thingverse.com – (Website offering multiple design files)
Category | # of files | # of instructions
Industrial tools | 23 | 27.2 Million
Hobby items | 34 | 16.5 Million
Household items | 19 | 5.4 Million
… | … | …
12 Categories | 338 files | 71 million instr.

## Slide 17
Insights from Energy Analysis
Motors consume the
most energy; not the heaters
Insight: Power-gating the motor can drastically reduce energy consumption
Chart: 
| Heater | Fans | Others | Motors
Column1 | 40.4 | 6.9 | 1 | 51.7
Simulation over 338 Designs

## Slide 18
Talk Outline
Application
Layer
Compiler
Layer
Firmware
Layer
STL
G-code
Signal
Hardware
Layer
1. Background
2. Instruction-level Energy Analysis
Instruction
Support
Firmware
Support
Compiler
Support
3. Cross-layered Energy Optimizations
4. Evaluation
Square Circles
Lines
Grid
Triangles

## Slide 19
Cross-Layer Energy Reduction Approach for 3D Printers
Instruction
Support
Firmware
Support
Compiler
Support

## Slide 20
Cross-Layer Energy Reduction Approach for 3D Printers (1/6)
Application
Layer
Compiler
Layer
Firmware
Layer
Hardware
Layer
STL
G-code
Signal
Firmware Support Interface
Re-compiler
S-series Instr.
Re-compiler Algorithm
New
G-code
Our Cross-
Layered Solution

## Slide 21
Cross-Layer Energy Reduction Approach for 3D Printers (2/6)
Instruction Support
New S-series G-code Instructions
S-series | Function | Pwr. (W)
S X on | X-motor on | 2.39
S X off | X-motor off | 2.38
S Y on | Y-motor on | 2.40
S Y off | Y-motor off | 2.42

## Slide 22
Cross-Layer Energy Reduction Approach for 3D Printers (3/6)
Addition of New S-series G-code Instructions
G1 X680.185 Y80.416 E1.15471
G1 X680.185 Y80.079 E1.24956
G1 X680.185 Y79.831 E1.33800
G1 X680.185 Y79.717 E1.38503
G1 X682.736 Y79.717 E1.47988
G1 X683.482 Y79.717 E1.57035
G1 X683.872 Y79.717 E1.61737
G1 X684.628 Y79.717 E1.70820
S X off
S Y on
G1 X680.185 Y80.416 E1.15471
G1 X680.185 Y80.079 E1.24956
G1 X680.185 Y79.831 E1.33800
G1 X680.185 Y79.717 E1.38503
S Y off
S X on
G1 X682.736 Y79.717 E1.47988
G1 X683.482 Y79.717 E1.57035
G1 X683.872 Y79.717 E1.61737
G1 X684.628 Y79.717 E1.70820
S Instructions
S Instructions
Original G-code File
Instruction Support

## Slide 23
Cross-Layer Energy Reduction Approach for 3D Printers (4/6)
Firmware Support
Extension of firmware to facilitate individual motor control
Significant Changes in Firmware:
In Hardware Driver Management:
- Power Gate X, Y and Z motors.
In Execution loop:
- Back-up Current Motor direction.
- Interpret new S-series instructions.
Stepper Motor Driver
Stepper Motor Driver
Stepper Motor Driver
CONTROL
X Motor
Y Motor
Z Motor
PWM
PWM
PWM
INV
INV
INV
UNIT
Enable
Enable
Enable

## Slide 24
Cross-Layer Energy Reduction Approach for 3D Printers (5/6)
Incorporation of Unique Cyber-Physical Systems Properties
X-Axis
Y-Axis
X-Axis
Y-Axis
Nozzle
X-Motor switch on
Instruction Inertia
Instruction Delay
Compiler Support
Y-Motor switch off

## Slide 25
Cross-Layer Energy Reduction Approach for 3D Printers (6/6)
Compiler Support
3. S-series Insertion
S X off
S Y on
G1 X680.185 Y80.416 E1.15471
G1 X680.185 Y80.079 E1.24956
G1 X680.185 Y79.831 E1.33800
G1 X680.185 Y79.717 E1.38503
S Y off
S X on
G1 X682.736 Y79.717 E1.47988
G1 X683.482 Y79.717 E1.57035
G1 X683.872 Y79.717 E1.61737
G1 X684.628 Y79.717 E1.70820
Chart: 
 | 100 | 100 | 100 | 100 | 100
 | 75 | 75 | 75 | 75 | 75
2. Model Rotation in 2D
1. Instruction Grouping
G1 X680.185 Y80.416 E1.15471
G1 X680.185 Y80.079 E1.24956
G1 X680.185 Y79.831 E1.33800
G1 X680.185 Y79.717 E1.38503
G1 X682.736 Y79.717 E1.47988
G1 X683.482 Y79.717 E1.57035
G1 X683.872 Y79.717 E1.61737
G1 X684.628 Y79.717 E1.70820
Re-compiling Algorithm
(Implemented in CURA Engine)

## Slide 26
Instruction Category | Old Pwr. (W) | New Pwr. (W) | % Reduction
G0 7200 mm/min | 21.30 | 21.30 | -
G1 1200 mm/min | 37.90 | 24.12 | 36.4%
G1 3600 mm/min | 39.94 | 24.69 | 38.2%
G1 5200 mm/min | 40.38 | 24.54 | 39.2%
G1 8600 mm/min | 42.06 | 26.90 | 36.0%
M109: Heater Temp | 31.19 | 31.19 | -
M106: Fan on | 3.61 | 3.61 | -
Results of Cross-Layer Energy Reduction Approach
Reduction in Power Consumption by our Cross-Layered Approach

## Slide 27
Talk Outline
Application
Layer
Compiler
Layer
Firmware
Layer
STL
G-code
Signal
Hardware
Layer
1. Background
2. Instruction-level Energy Model
Instruction
Support
Firmware
Support
Compiler
Support
3. Cross-layered Energy Optimizations
4. Evaluation
Square Circles
Lines
Grid
Triangles

## Slide 28
Evaluation
Benchmark
338 Benchmark files
71 million lines of G-code
Evaluation on four in-fill patterns
Square Circles
Lines
Grid
Triangles

## Slide 29
Evaluation
Average energy reduction : 25%
Chart: Energy Reduction (%)
| 0.0 | 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0
# of G-code Files | 18 | 40 | 47 | 60 | 31 | 118 | 32 | 5 | 5
Avg. 25%

## Slide 30
Evaluation
Sensitivity of different in-fill patterns
(6 prints on real printer)
Insight: Square Circles in-fill is best pattern for power-gating

## Slide 31
Evaluation
Chart: Increase in File Size (%)
| 0.0 | 0.25 | 0.5 | 0.75 | 1.0 | 1.25 | 1.5 | 1.75 | 2.0
# of G-code Files | 20 | 78 | 91 | 80 | 23 | 21 | 17 | 3 | 2
Effect on G-code File Size
Effect on Print Duration
Chart: Time to Print (seconds)
| Hinge | 3D Puzzle | Cup Holder | Whistle | IPhone5 Cover | Gear
Default | 12000 | 7500 | 23000 | 5000 | 6500 | 2300
3DGates | 12000 | 7500 | 23000 | 5000 | 6500 | 2300
Max. 2%
Insight: No increase in storage
Insight: No increase in print time

## Slide 32
Evaluation
Above all: No Effect in Print Quality

## Slide 33
Conclusion
Instruction Level Energy Analysis is viable for simulating energy consumption in 3D Printers.
Motors consume significant energy in 3D Printers.
A cross-layered software only solution reduces energy consumption by 25%.
Chart: 
 | 40.4 | 6.9 | 1 | 51.7
Chart: 

## Slide 34
Miscellaneous

## Slide 35
Miscellaneous
Energy Consumption at different orientations in 2D

## Slide 36
An accurate instruction-level energy consumption model for embedded RISC processors
ACM SIGPLAN 2001.
Instruction level power analysis and optimization of software
Technologies for wireless computing, Springer, 1996.
Powerscope: A tool for profiling the energy usage of mobile applications
WMCSA'99.
Instruction Level Energy Studies